## Slide 1: BEGINNER EV3 PROGRAMMING Lesson
By: Droids Robotics
Topics Covered:
Ultrasonic Sensor

## Slide 2: LESSON OBJECTIVES
Learn about the Ultrasonic Sensor
Learn how to use Wait Until Ultrasonic Block
Learn the difference between the Wait Until Ultrasonic Block and the Ultrasonic Block

## Slide 3: What is a sensor?
A sensor lets an EV3 program measure and collect data about is surroundings
The EV3 sensors include:
  Colour – measures color and darkness
  Gyro – measures rotation of robot
  Ultrasonic – measures distance to nearby surfaces
  Touch – measures contact with surface
  Infrared – measures IR remote’s signals
Image from: http://www.ucalgary.ca/IOSTEM/files/IOSTEM/media_crop/44/public/sensors.jpg
Our lessons will cover the all the sensors

## Slide 4: Ultrasonic CHALLENGE 1
Challenge: Make the robot move until it is 5 inches away from the wall.
Step 1: Make a new program
Step 2: Set move to “on”
Step 3: Set wait block to use the Ultrasonic
Step 4: Set move block to “off”

## Slide 5: Challenge 1 solution

## Slide 6: Challenge 2: Dog Follower
If the robot is closer than 5 inches away from your hand move backward, otherwise move forward.
Step 1: Drag a loop from the orange tab
Step 2: Drag switch inside loop
Step 3: Set switch to Ultrasonic
Step 4: Set move steering block to ON and place in TRUE
Step 4: Set move steering block to OFF and place in FALSE

## Slide 7: Challenge 2 solution

## Slide 8: Robots can follow you & even dance with this code!

## Slide 9: CREDITS
This tutorial was created by Sanjay Seshan and Arvind Seshan from Droids Robotics.
More lessons are available at www.ev3lessons.com
Author’s Email: team@droidsrobotics.org
This work is licensed under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.