## Slide 1: BEGINNER EV3 PROGRAMMING Lesson
By: Droids Robotics
Topics Covered:
Ultrasonic Sensor

## Slide 2: LESSON OBJECTIVES
Learn about the Ultrasonic Sensor
Learn how to use Wait Until Ultrasonic Block
Learn the difference between the Wait Until Ultrasonic Block and the Ultrasonic Block

## Slide 3: What is a sensor?
A sensor lets an EV3 program measure and collect data about is surroundings
The EV3 sensors include:
  Color – measures color and darkness
  Gyro – measures rotation of robot
  Ultrasonic – measures distance to nearby surfaces
  Touch – measures contact with surface
  Infrared – measures IR remote’s signals
Image from: http://www.ucalgary.ca/IOSTEM/files/IOSTEM/media_crop/44/public/sensors.jpg

## Slide 4: ULTRASONIC
An ultrasonic sensor measures distance.
You use it when you need to make sure you are a certain distance away from a target.
The distance can be measured in inches or centimeters.
To read the ultrasonic sensor, you use the Ultrasonic Block. To use the ultrasonic to do an action until a distance, you use “Wait Until”
Wait for Ultrasonic
Read Ultrasonic
VS.

## Slide 5: Ultrasonic CHALLENGE 1
Challenge: Make the robot move until it is 20cm away from the wall.
Step 1: Make a new program
Step 2: Set move to “on”
Step 3: Set wait block to use the Ultrasonic
Step 4: Set move block to “off”

## Slide 6: Challenge 1 solution

## Slide 7: CHALLENGE 2: Use The Force To Control Your Robot!

## Slide 8: Challenge 2: PSEUDOCODE
If the robot is closer than 20cm away from your hand move backward, otherwise move forward.
Step 1: Drag a loop from the orange tab
Step 2: Drag a switch inside loop
Step 3: Set switch to Ultrasonic
Step 4: Set move steering block to ON with negative power and place in TRUE
Step 4: Set move steering block to ON with positive power and place in FALSE

## Slide 9: Challenge 2 solution

## Slide 10: Learning To Master Your Force
The previous code kept the robot moving always. This version lets the robot rest if it is between 15-20 centimeters.

## Slide 11: CREDITS
This tutorial was created by Sanjay Seshan and Arvind Seshan from Droids Robotics.
More lessons are available at www.ev3lessons.com
Author’s Email: team@droidsrobotics.org
This work is licensed under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.