## Slide 1: BEGINNER PROGRAMMING LESSON
Sound Block

## Slide 2: LESSON OBJECTIVES
Learn to use the Sound Block
Understand why the Sound Block can be useful in programming

## Slide 3: Sound Block
The Sound Block plays sounds to the EV3
You can play files, tones, and notes
Located in Green Tab

## Slide 4: MORE ON Sound Blocks
Four Modes
Stop
  Stop playing any sounds
Play File
  Play a .rsf sound file
  This is used for playing sounds (eg. Hello)
Play Tone
  Play any music note (eg. D, D#)
  Also plays custom frequencies via a data wire
Play Note
  Play a key on a piano

## Slide 5: Inputs
Volume of sound
Wait for the sound to finish before moving on
Sound file name
Frequency/Note of sound
Duration of sound
Piano note to play
A
B
C
D
E
A
B
F
E
A
B

## Slide 6: Sound BLOCK CHALLENGE 1
Make a program that plays hello after you press the touch sensor
Hints:
  You will have to use a wait block
  You will have to use the sound block in File mode

## Slide 7: Challenge 1 solution
Wait for touch
Play Hello

## Slide 8: Sound block CHALLENGE 2
Pick up your robot and place it on different colors. Check if the color sensor reads black. If so, have the robot say “black”. If the color sensor sees red, have the robot say “red”
For any other color, play a note of your choice for 0.01 seconds
Make sure that the sound waits for completion
Repeat this forever
Bonus Challenge: Can you the above while having the robot move? Have the robot drive over different colors to test your code

## Slide 9: Challenge 2 Solution
Switch set to measure color
If Black, play Black
If Red, play Red
Set as default
Play a note for any other color
Loop forever

## Slide 10: Challenge 2 Bonus Solution
Move on at 10 power
Switch set to measure color
If Black, play Black
If Red, play Red
Set as default
Play a note for any other color
Loop forever

## Slide 11: Additional Challenges
Add more colors to the switch so that as the robot drives over additional colors, it say “green”, “blue”, “yellow”, etc.
Make the code stop after the robot detects 5 colored bands

## Slide 12: Discussion Guide
Why might you want to know how to use the sound block?
  You might want to know what part of the code you are at. See Debugging lesson in Intermediate
  The sound block is a fun way to add emotion to your robot
  You can use sounds to interact with the user in a game by saying “good job”, “game over”, etc.

## Slide 13: CREDITS
This tutorial was created by Sanjay Seshan and Arvind Seshan
More lessons are available at www.ev3lessons.com
This work is licensed under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.