## Slide 1: Line Following with Two Color Sensors and Proportional Control
By Droids Robotics
Code Contributed by FLL 1920
ADVANCED EV3 PROGRAMMING LESSON

## Slide 2: Objectives
Learn how to write a line follower that uses two color sensors
Learn how to write a two color line follower that uses proportional control
Pre-requisites: Basic Line Following, Switches, Loops, Proportional Control

## Slide 3: A Basic One Sensor Line Follower
Robot sees white, turn left
Robot sees black, turn right

## Slide 4: What is a Two Color Line Follower?
The goal is to use two light sensors next to each other to follow a line
The light sensors need to be placed approximately the line’s width apart
When following the line they should both sensors should be reading the edge of the line
Watch video to see line straddling in action

## Slide 5: Tips for success
Placement of the two color sensors are very important
In the picture on the right, we have a beam placed so you can see how far apart to place your sensors.

## Slide 6: Two Color Sensor Line Follower
2
1
Sensor 1 on White
Sensor 2 on White
Go forward
Sensor 1 on Black
Sensor 2 on White Turn left
Sensor 1 on White
Sensor 2 on Black Turn right
2
1
2
1

## Slide 7: Challenge 1
Use the ideas from Slide 4 and write a line follower that straddles a red line – uses 2 color sensors to line follow a red line?
2
1
Sensor 1 on White
Sensor 2 on White
Go forward
2
1
2
1
Sensor 1 on Red
Sensor 2 on White Turn left
Sensor 1 on White
Sensor 2 on Red Turn right

## Slide 8: Challenge 1 Solution

## Slide 9: How do you add proportional control?
What is the target  both sensors should read the same value
What is the error  the difference between the sensors
What is the correction  turn more sharply if the difference is large
2
1
Sensor 1 reading 50
Sensor 2 reading 50
Go forward
2
1
2
1
Sensor 1 reading 10
Sensor 2 reading 100 Turn Left sharply
Sensor 1 reading 60
Sensor 2 reading 40 Turn right slightly

## Slide 10: Challenge 2 Solution

## Slide 11: Watch this code in action on YouTube
EV3Lessons.com YouTube Channel

## Slide 12: Credits
This lesson was written by Droids Robotics using code, video and photos by FLL Team 1920.
More lessons are available at www.ev3lessons.com
This work is licensed under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.