## Slide 1: Data Logging (Part 1)
ADVANCED EV3 PROGRAMMING LESSON
By Droids Robotics

## Slide 2: Lesson Objectives
Learn what data logging is
Learn the different ways of doing data logging on the EV3
Learn how to use the Live Data Logging, Remote Data Logging and Brick Data Logging feature using a temperature sensor
Prerequisites: Must own an NXT Temperature Sensor, Must have the Edu version of the EV3 Software and Edu version of brick firmware.

## Slide 3: What is Data Logging?
The EV3 software provides a simple way to continuously record sensor readings to a file and to plot the values later. This is called Data Logging.
Why use Data Logging:
  Great for science experiments. In this lesson, we will show how you can record values like temperature for a science project.
  Great for understanding robot programming blocks. In the next lesson, we will show how to use data logging to measure the difference between turns.
  Great for understanding sensor behavior. In the third lesson, we will show how to use data logging to understand the details of sensors such as the gyro sensor.

## Slide 4: How do you data log on an EV3?
  Live Data Logging: Real time data collected directly in the EV3 software
  Remote Data Logging: Use the the brick to collect data, and transfer the data to the computer for analysis
  Brick Data Logging: Run the experiment directly from the brick
  Autonomous. Collect data with the Data Logging block. The data is stored on the brick.
Lesson 1: Temperature Sensor Experiment
Lesson 2: Differences Between Turns
There are 4 ways to data log using the EV3 MINDSTORMS:

## Slide 5: Live Data Logging
Challenge: We will use a Temperature Sensor to log the changing temperature of water.
Design your own experiment. For example, you can try placing the temperature sensor probe at room temperature water, then boiling water and then cold water.

## Slide 6: Live Data Logging (Temperature Sensor)
STEP 1:
Start a New Experiment in an existing project
STEP 2:
Turn off Oscilloscope Mode
STEP 3: Pick your duration, sample rate, sensor and units.

## Slide 7: Live Data Logging (Temperature Sensor)
STEP 4:
All sensors connected to the EV3 will be automatically added. If you do not want to collect data with a particular sensor, click the “X” next to it.
STEP 6: Place temperature probe in hot/cold liquid and watch the graph (see next slide)
STEP 5: Download and Run

## Slide 8: Results/Solution
1. Room temperature probe placed in boiling water
2. Temperature increases
3. Probe removed and placed in cold water
A similar graph will appear live on your screen.

## Slide 9: Other Ways to Collect Data
Now that we have tried Live Data Logging, let’s look at two other ways to collect data when the computer isn’t around:
  Remote Data Logging: Use the the brick to collect data, and transfer the data to the computer for analysis
  Brick Data Logging: Run the experiment directly from the brick

## Slide 10: Remote Data Logging Instead
STEP 6: Take your robot somewhere else and run the experiment from the screen
STEP 7: Place temperature probe in hot/cold liquid
STEP 1-4: Repeat steps 1-4 of the Live Data Logging
STEP 8: Connect your robot and click on the Upload Icon. In the Data Log File Manager, pick the correct file to import.
Upload Icon
Download Icon
STEP 5: Click on the Download icon
These icons appear only when you are in an open EXPERIMENT (not a Project)

## Slide 11: Using Brick Data Logging Instead (Part 1)
STEP 2: Click on the wrench to set up sensors
STEP 4: Place temperature sensor probe in hot/cold liquid
STEP 1: Go to third tab on Brick Menu and pick Brick Datalog
Step 5: Click on the sphere icon to start and stop collecting data
STEP 3: Click on icon with numbers to see the data for a different sensor

## Slide 12: Brick Data Logging (Part 2)
Upload Icon
STEP 7: Connect your robot and click on the Upload Icon after you are in an Experiment. In the Data Log File Manager, pick the correct file to import.
STEP 6: Pick name for the file on the brick
These icons appear only when you are in an open EXPERIMENT (not a Project)

## Slide 13: Next Steps
Can you think of other experiments?
Try data logging using other sensors.
Try exporting your data into Excel or another spreadsheet tool.
Learn how to use Autonomous Data Logging in Part 2 of the Data Logging series of lessons.

## Slide 14: Credits
  This tutorial was written by Sanjay Seshan and Arvind Seshan from Droids Robotics
  More lessons at www.ev3lessons.com
This work is licensed under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.