## Slide 1: Ramping Up Speed
By Mesa Robles Robotworks
and Droids Robotics
ADVANCED EV3 PROGRAMMING LESSON

## Slide 2: Lesson Objectives
Learn what ramp up means
Learn how and when to use ramp up
Learn how to use the Timer Block
Prerequisites: Data Wires, My Blocks with Inputs & Outputs

## Slide 3: Why Ramp Up
Ramping up speed is very helpful when running fast-paced programs
Usually, if the robot starts up with high speed, then there would be a small jolt in the beginning. The jolt may change the position of the robot.
With the ramp up, it would start up slowly and increase speed over time (see video on the right)

## Slide 4: New Tool: Timer Block
The timer block is used to count time
It is found in the Yellow (sensor tab) in the EV3 Software.
Multiple timers are available (up to 8 timers)
You can use the block to reset a specific timer back to 0 secs
You can use the block to output the time since reset…
If you are an FLL team, you can use timers to track time or for the ramp up code in this lesson
Timer no.
Elapsed time for that timer

## Slide 5: Ramp Up Challenge 1
Challenge: Write a simple ramp up program that gradually increases the speed by 20 every second for 5 seconds.
Pseudocode:
1. Reset timer
2. In a loop, read the number of seconds passed and multiply the power by 20.
3. Still in the loop, take the result of the multiplication and connect it to the move block.
4. Repeat the Loop for 5 seconds
5. Once the program exits the loop, stop the motor

## Slide 6: Challenge 1 Solution
Code by Mesa Robles Robotworks. Modified by Droids Robotics

## Slide 7: Ramp Up Challenge 2
Step 1: Can you now make a ramp up program that takes 2 inputs (total duration of ramp up and how much you want the motor to ramp up per second)? Create a My Block.
Step 2: Ramp up your robot, then move until a black line.

## Slide 8: Creating the My Block
Code by Mesa Robles Robotworks. Modified by Droids Robotics

## Slide 9: Inside the My Block
Code by Mesa Robles Robotworks. Modified by Droids Robotics

## Slide 10: Challenge 2 Solution
Code by Mesa Robles Robotworks. Modified by Droids Robotics

## Slide 11: Discussion Guide
What is ramping up? Ans. Ramping up is starting slow and getting gradually faster.
Why should you bother? Ans. Ramping up can reduce sudden jerk in robot movement.

## Slide 12: Next Steps
Think about what else you might be able to use a timer block for.

## Slide 13: Credits
  This tutorial was created by Mesa Robles Robotworks (mesarobotworks@gmail.com)
  Droids Robotics added content to complement the original lesson (team@droidsrobotics.org)
  More lessons at www.ev3lessons.com
This work is licensed under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.