## Slide 1: INTERMEDIATE PROGRAMMING LESSON
LOGIC OPERATIONS & DECISION MAKING

## Slide 2: Lesson Objectives
Learn what the Logic Block does
Learn how to use the Logic Block
Prerequisites: Data Wires, Sensor Blocks

## Slide 3: Logic Operations Block
The Logic Bock does a Logic operation on its inputs, and outputs the result
A Logic Block takes inputs that are True or False, and produces a True or False output
Logic values can be used as inputs into loop exists and switch conditions.
It is found in the Red Programming Pallet tab
Mode
Inputs
Output/Result

## Slide 4: Different Modes in the Logic Block
Icon | Mode | Inputs | Output/Result
 | AND | A, B | True if both A and B are both true, otherwise the result is False
 | OR | A, B | True if either A or B (or both) is/are True. The result is False if both A and B are False
 | XOR | A, B | True only if one (and exactly one) of A and B is True The result is False if both A and B are True The result is False if both A and B are False
 | NOT | A | Outputs the opposite of what you input. The result is True if A is False The result is False if A is True
The icons are Venn Diagrams. The dark shaded areas identify what needs to happen for the block to output True.

## Slide 5: Logic Blocks in Three Easy Steps
CHALLENGE: Make your robot drive forward until EITHER the Touch Sensor is pressed or the Color Sensor detects black.
STEP 1: Turn the motors on
STEP 2: Add the Logic and Sesnsor Blocks
  A. Use a Logic Block in the OR mode
  B. Add the inputs: Take a color sensor and a touch sensor blocks and wire them into the Logic Block as inputs
STEP 3: Add a Loop and loop exit condition:
  Place the Sensor and Logic Blocks in a loop
  For the exit condition of the loop, select logic. Wire the result of the Logic Block into the exit condition
  If the result of STEP 2 is True, you should exit the loop and stop the robot

## Slide 6: Challenge Solution
STEP 1
STEP 2
STEP 3

## Slide 7: Credits
  This tutorial was written by Sanjay and Arvind Seshan from Droids Robotics. To contact the authors, email team@droidsrobotics.org
  More lessons at www.ev3lessons.com
This work is licensed under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.