## Slide 1: BEGINNER PROGRAMMING Lesson
By: Droids Robotics
Basic Line Follower

## Slide 2: LESSON OBJECTIVES
Learn how humans and robots follow lines
Learn how to get a robot to follow a line using Color Mode on the EV3 Color Sensor
Learn how to follow a line until a sensor is activated
Learn how to follow a line for a particular distance
Learn how to combine sensors, loops and switches

## Slide 3: TEACHER INSTRUCTIONS
Slides 4-7 are animated. For students to better understand how a line follower works and how a human and a robot follow a line, we recommend that you play the animation
Give each student/team a copy of the worksheet.
Challenge 1 begins on slide 10 and Challenge 2 on Slide 13
Discussion Guide is on Slide 16
More advanced students might be interested in other line followers on EV3Lessons.com

## Slide 4: FOLLOW THE MIDDLE?
Humans want to follow the line in the middle.
Let’s have the robot do the same thing using the Color Sensor
What type of questions can we ask using this sensor
  Are you on line or not?

## Slide 5
If we are on black, keep going straight
If we are on white, turn left to get back to the line
Seems to work fine here…

## Slide 6
If we are on black, keep going straight
If we are on white, turn left to get back to the line
OH NO… my robot is running away….
When the robot leaves the left side of the line, the program no longer works!

## Slide 7: Line Following: ROBOT STYLE
Why could the Human follow the middle?:
  They can see ahead.
  They can see the whole line and its surroundings
  They see both sides and which side they left
Why can’t the Robot do the same thing?:
  Can’t tell right or left side of the line
  How do we make sure the robot always veers off on the SAME SIDE of the line?
    Instead of the middle, could the robot follow the “edge”?
  So now the robot will fall off only the same side.
  We will now show you how this works!

## Slide 8: ROBOT LINE FOLLOWING Happens on the edges
Left side line following
Right side line following
The robot has to choose which way to turn when the color sensor sees a different color.
The answer depends on what side of the line you are following!
If on black, turn left.
If on white turn right.
If on black, turn right.
If on white turn left.

## Slide 9: starting the roboT on the correct side
✔
✗
✔

## Slide 10: Line Follower challenge 1
Step 1: Write a program that follows the RIGHT edge of a line.
Hints: If your sensor sees black, turn right. If your sensor sees white, turn left. Use loops and switches!
Step 2: Try it out on different lines.
Did your line follower work the same on straight and curved lines?
Step 3: If not, instead of turn Steering = 50, try smaller values.
Is it better on the curved lines now?
B
C
B
C

## Slide 11: LINE FOLLOWING CHALLENGE SOLUTION
Q. Does this program follow the Right or Left side of a line?
A. The robot is following the Right Side of the line.
Notes: Right side

## Slide 12: CHALLENGE 1 SOLUTION
Q. This line follower goes forever. How do we make this stop?
A. Change the end condition on the loop.
Notes: Right side

## Slide 13: Line follower challenge 2
Part 1: Make a line follower that stops when you press the touch sensor
Part 2: Make a line follower that stops after it travels a particular distance

## Slide 14: Challenge 2 SOLUTION: SEnsor

## Slide 15: Challenge 2 SOLUTION: PARTICULAR distance

## Slide 16: DISCUSSION GUIDE
Why is it important for the robot to follow the same side of the line?
The robot only knows to check if it is on or off the line.
This is a basic line follower. What are some things that were not good about this line follower? Do you think the line follower can be improved?
It wiggles a lot. Smoother line followers are described in the Advanced lessons
What sensor measures how far you have travelled?
The rotation sensor used in Challenge 2 solution measures how much the wheels have turned
How would you write a line follower that will stop when it sees a line? Or another color?
Change the loop exit condition to use the color sensor.

## Slide 17: CREDITS
This tutorial was created by Sanjay Seshan and Arvind Seshan from Droids Robotics.
More lessons are available at www.ev3lessons.com
Author’s Email: team@droidsrobotics.org
This work is licensed under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.